## Slide 1
1

## Slide 2: Contents
2
1.
Core Concepts
3
2.
Insta360 One R: Hardware
9
3.
Insta360 One R: Software
17
4.
Insta360 Studio: Editing
28
5.
Publishing
42
References
44
MCL

## Slide 3: 1. Core Concepts
3
MCL

## Slide 4: 1.1. Core Concepts: Form
4
  Lenses (2+) facing different direction
      Blind spots
  Built-in software stitches imagery together
      Other functions: Stabilization, object removal
MCL

## Slide 5: 1.2. Core Concepts: Function
5
  Spaces
      Entire physical environments
  Scenes
      Entire group of activities/subjects
  Scenarios
      Places of pertinent possibility
MCL

## Slide 6: 1.3. Core Concepts: Discretion
6
  Intended communication?
      Mona Lisa vs Mona Lisa in the Salle Des États
  Safety/security?
      Mobile vs stationary
  Informed consent?
      Public settings
  Duration?
      One R battery: ~45 min at highest settings
MCL

## Slide 7: 1.4. Core Concepts: Photography
7
Three settings affect exposure to light:
  Aperture (F-Stop): Size of lens opening
      Pupil of eye
  Shutter speed: Time of lens exposure
      Blink of eyelid
  ISO
  Exposure value (EV): Aperture & shutter speed
  Use Automatic settings or research Manual settings
MCL

## Slide 8: 1.5a. Core Concepts: Manual Settings
8
Suggested base-settings for outdoor environments:
Color
Shutter speed
ISO
White Balance
Sunny
Vivid
1/200
100 - 400
5500K
Cloudy
Standard 1/60 - 1/200 400 - 800 6000k - 7000k
MCL
(Wilkerson, n.d.; Rossi, 2023)

## Slide 9: 1.5b. Core Concepts: Manual Settings
9
Suggested base-settings for indoor environments:
Color
Shutter speed
ISO
White Balance
Bright
Vivid
1/50 (tripod)
1/60 - 1/200
800
2800K
Dim/Shaded
Standard 1/50 (tripod) 1/60 - 1/200 1600+
7500K
MCL
(Wilkerson, n.d.; Rossi, 2023)

## Slide 10: 1.6. Core Concepts: Basic Tips
10
  Seek uniform lighting to mask stitching
  Wipe lenses with microfibre cloth
  Identify blind spots where stitching can be obvious
  Aim main lens at main element in scene
  Suppress BG noise: Settings -> Wind Noise Reduction
MCL

## Slide 11: 2. Insta360 One R: Hardware
11
MCL

## Slide 12: 2.1. One R Hardware: Overview
12
  Modular system
      Battery base
      Core module (touchscreen, buttons, ports)
      Lens module: dual-lens, wide-angle, or 1-inch
  Image recording
      Photos, videos, webcam
  Image effects
      Bullet Time, Time Lapse, Tiny Planet
MCL

## Slide 13: 2.2. One R Hardware: Core Module
13
  Touchscreen
  Top buttons
      Power button (smaller, I/O icon)
      Shutter button (larger, red circle icon)
  Side openings (behind cover)
      MicroSD card (file storage)
      USB-C cable (charging, file transfer, input)
MCL

## Slide 14: 2.3. One R Hardware: Dual-Lens Mod
14
  Front and back lenses
      Back lens: Beside touchscreen
      Field of view: Less than 180 degrees
      Blind spots: Sides, top, & bottom of module
MCL

## Slide 15: 2.4. One R Hardware: Battery Base
15
  Notch inserts (top)
      Pair with notches underneath connected core & lens
  Slide lock
      Hold to remove battery
      Visible yellow: Improper/loose connection
  Battery life
      Max resolution/framerate: ~45 min
      Drains while turned off: Remove while storing
MCL

## Slide 16: 2.5. One R Hardware: Mount Bracket
16
Open bracket:
  Locate slide-lock on buckle (top)
  Push slide-lock (direction of arrow) & hold
  Lift bottom-edge of buckle (Point to Track side)
  Lift top-edge of buckle
  Open ramp at back of bracket
  Insert/remove camera through back of bracket
MCL

## Slide 17: (continued)
17
Close bracket:
  Insert/remove camera through back of bracket
  Close ramp at back of bracket
  Hook back-edge of buckle onto top-edge of ramp
  Press (snap) front-edge of buckle onto top of bracket
MCL

## Slide 18: 2.6. One R Hardware: Selfie Stick
18
(Optional) Connect to tripod:
  Screw top (or side) of tripod into Selfie Stick (bottom)
  Screw Selfie Stick (top) into bracket hinge (bottom)
  (Optional) Grab neck (ribbed top) of Selfie Stick & pull
  Software removes Selfie Stick from underside blind spot
MCL

## Slide 19: 2.7. One R Hardware: Tripod
19
(Optional) Connect to Selfie Stick or camera (bracket)
  Screw top (or side) of tripod into Selfie Stick or bracket
  Hold (folded) tripod legs
  Hold section (top) housing screws
  Twist ribbed ring-lock until tight
MCL

## Slide 20: 3. Insta360 One R: Software
20
MCL

## Slide 21: 3.1. One R Software: Touchscreen
21
  Long-press power button (smaller button on top)
  Swipe touchscreen to view option screens
      System settings: Downward (from top)
      Media Gallery: Upward (from bottom)
      Recording modes: Rightward (from left)
      Recording parameters: Leftward (from right)
  (Alternative) Select mode/parameters from main screen
MCL

## Slide 22: 3.2. One R Software: Recording
22
  Select recording mode
  (Optional) Change camera parameters*
  (Optional) Change resolution/frame-rate
  Long-press shutter button (top) to record
  (Video) Long-press shutter button to stop
*Consider settings listed in Section 1.5 (8-9)
MCL

## Slide 23: 3.3. One R Software: Serial Number
23
Get serial number of camera:
  (Main screen) Swipe downward
  (System screen) Swipe rightward to page 2
  Select Settings (gear icon)
  Scroll to end of Settings screen & select Camera Info
  Note serial number (SN)
MCL

## Slide 24: 3.4. One R Software: Mobile Device
24
Set up mobile device:
  Enable Wi-Fi
  Enable Bluetooth
  Download Insta360 app (App Store or Google Play)
  Install app
  Note: Mobile app mirrors camera
MCL

## Slide 25: 3.5. One R Software: Mobile App
25
Pair mobile app/device & camera:
  Open Insta30 app
  Grant necessary permissions
  Select Go to App button
  Select Connect button (or camera icon in toolbar)
  Turn on camera
  (Camera) Select Confirm connection
  Select Join for camera to join app network
MCL

## Slide 26: 3.6. One R Software: Recording (App)
26
  Select camera icon (toolbar)
  (Optional) Select mode (bottom of UI)
  (Optional) Select parameters* (next to Record button)
  Press Record button (circle icon)
  (Video) Press Record button to stop
*Consider settings listed in Section 1.5 (8-9)
MCL

## Slide 27: 3.7. One R Software: View (App)
27
  (If applicable) Exit recording screen
  Select Album from toolbar
  Select recording (photo/video)
  (Optional) Select Export button
MCL

## Slide 28: 4. Insta360 Studio: Editing
28
MCL

## Slide 29: 4.1. Editing: Insta360 Studio Overview
29
  Proprietary software (free)
      https://www.insta360.com/download/insta360-oner
  Download page requires serial number
      Follow steps in section 3.3
      Enter IAEAH14BRWSRX9
  Includes plugins for third-party software
      Adobe Premiere, Final Cut Pro
MCL

## Slide 30: 4.2a. Editing: File Transfer (USB)
30
  Select Settings (gear icon) -> General -> USB Mode
  Select U-Disk Mode
  Open side cover of core module
  Use USB cable to connect camera & computer
  Turn on camera
  Locate camera as disk drive on computer
  Navigate to DCIM -> Camera01
  Copy files to computer
MCL

## Slide 31: 4.2b. Editing: File Transfer (MicroSD)
31
  Turn off camera (long-press power button)
  Open side cover of core module
  Press exposed edge of MicroSD card & remove
  Insert MicroSD card into SD card adapter
  Insert card adapter into computer
  Locate camera as disk drive on computer
  Navigate to DCIM -> Camera01
  Copy files to computer
MCL

## Slide 32: 4.3. Editing: Studio UI
32
  Menu bar
      Essential actions/commands
  Left panel: Files
      Importing/imported files & rendering files (export)
  Middle panel: Playback/editing
      Image area, frame parameters & actions
      Toolbars, timeline, export button
  Right panel: Parameters/projects/properties
MCL

## Slide 33: 4.4. Editing: Studio Timeline
33
  Playhead: Large, white line
      Click timeline to set
  Skimmer: Thin, yellow line
      Move cursor along timeline
  Trim start/end: Shorter, white lines
      Mark start/end of exported project
      Drag to spot or click Mark [...] start/end (at playhead)
MCL

## Slide 34: 4.5. Editing: Playback Shortcuts
34
  Play/pause/resume: Space
  Skip to trim-start: [
  Skip to trim-end: ]
  Zoom out timeline: Ctrl/Cmd + Minus key (-)
  Zoom in timeline: Ctrl/Cmd + Equals key (=)
  Forward/backward 1 frame: Right/Left
  Forward/backward 10 frames: Shift + Right/Left
  Increase/decrease volume: Up/Down
MCL

## Slide 35: 4.6. Editing: Playhead Shortcuts
35
  Add trim start: Ctrl/Cmd + [
  Add trim end: Ctrl/Cmd + ]
  Add keyframe (Reframe View only): Ctrl/Cmd + K
      Set parameters (FOV, angles, etc) at specific point
MCL

## Slide 36: 4.7. Editing: Image Area (360 Video)
36
  Reframe View or 360 View (tabs above image)
  Changing shown-image:
      Click & drag: Change angle
      Mouse-scroll up: Zoom out
      Mouse-scroll down: Zoom in
  What you see is what you get with Export reframed video
MCL

## Slide 37: 4.8. Editing: Image Toolbar
37
  Lower-right corner of image area
  (Reframe View) Ratio: Change aspect-ratio
      Default: 16:9
  (360 View) Switch FOV: Change field-of-view
      Default: Fisheye
  Take Snapshot: Ctrl/Cmd + S
  Full Screen: Shift + Ctrl/Cmd + F
MCL

## Slide 38: 4.9. Editing: Editing Toolbar
38
  Between image area & timeline, right-side
  (Reframe View) Mark as keyframe: Mark transition
  (Reframe View) Deep Track: Focus on subject
  Follow prompts
  Time Shift: Slow down or speed up
  Starts at playhead, ends at click on timeline
  Motion Blur: Toggle on/off motion blur
MCL

## Slide 39: 4.10. Editing: Keyframe Parameters
39
  Views
      Default (fisheye), Crystal Ball, Tiny Planet, Natural
  Angles
      Pan: x-axis (horizontal)
      Tilt: y-axis (vertical)
      Roll: z-axis (canted)
  Field of view (FOV)
  Distortion
MCL

## Slide 40: 4.11. Editing: Right Panel
40
  Stabilization Type
  Stitching: Presets & customization
  Media Processing: Effects/filters for colour & audio
  Logo Settings: Watermark image
  Project Management:
      Projects: Sets of changes auto-saved to source files
  File Properties: Specifications of source file
MCL

## Slide 41: 4.12. Editing: Exporting Videos
41
  Click Start Export button (yellow square, beside timeline)
  Select export type:
      Export reframed video: 2D video
      Export 360 video: 360-degree video in suitable apps
  (Optional) Adjust parameters
  Set name & location
MCL

## Slide 42: 5. Publishing
42
MCL

## Slide 43: 5.1. Publishing
43
Video-hosting platforms:
    Facebook
    VeeR
    Vimeo
    YouTube
MCL

## Slide 44: References
44
MCL

## Slide 45: References
45
Rossi, T. (2023). Camera settings for portraits: Checklist for indoor & outdoor photoshoots. Fixthephoto. https://fixthephoto.com/camera-settings-for-portraits.html
Wilkerson, S. (n.d.). Color by Kelvin: A better approach to white balance. Click Community. https://www.theclickcommunity.com/blog/color-by-kelvin-a-better-approach-to-white-balance/
MCL

## Slide 46: Attribution
46
Content by Tim Huynh
This work is licensed under a
Creative Commons Attribution-NonCommercial 4.0 International License.
MCL