## Slide 1
1

## Slide 2
2
Contents
1.
History
3
2.
Types
6
3.
Workflow
9
4.
Recording (Zoom H4n)
21
5.
Recording Practice
31
6.
Editing (Audacity)
34
7.
Editing Practice
53
References
55
MCL

## Slide 3
3
1. History
Broadcasting by any other name
MCL

## Slide 4
4
1.1. History: Pre-Internet
  1901: Discovery of wireless broadcasting
  1920: First commercial radio station (US)
  1930s-1940s: "Golden Age of Radio"
  1930s: TV broadcasting
  1954: Colour TV
  1960s: Widespread TV adoption
MCL
(Britannica, 2010; Britannica, 2021; DARPA, n.d.; Wikipedia, 2022a; Wikipedia, 2022b)

## Slide 5
5
1.2. History: Internet & Beyond
  1969: ARPAnet
  1980s: Satellite broadcasting
  2001: Apple iPod
  c 2004: "Podcast"
  2005: Distribution on Apple iTunes
MCL
(Britannica, 2010; Britannica, 2021; DARPA, n.d.; Wikipedia, 2022a; Wikipedia, 2022b)

## Slide 6
6
2. Types
Tried-and-true genres & formats
MCL

## Slide 7
7
2.1. Types: Genre
  Culture/entertainment
  Education/information
  News/politics
  Self-help
  True crime
MCL

## Slide 8
8
2.2. Types: Format
  Debates/discussions
  Interviews
  Recaps
  Reports
MCL

## Slide 9
9
3. Workflow
Planning, producing, & publishing
MCL

## Slide 10
10
3.1. Planning: Starting With The End
  Audience?
      Familiarity with topic(s)
      Personal factors
      Situational factors
  Technical specs?
      Duration
      File format/quality/size
      Volume in decibels (dB)
MCL
(Glendon Digital Media Lab, 2018a)

## Slide 11
11
3.2. Planning: Job To Be Done
Imagine your podcast is a product:
  What ‘job’ are listeners ‘hiring’ your podcast to do?
  What are their ‘requirements’ for the ‘job’?
MCL
(e.g. Christensen, 2019)

## Slide 12
12
3.3. Planning: Building a Story
  Story ‘question’?
      "Will ... ?," “Can ...?,” “Do ... ?,” “How ...?,” “Why ... ?”
  Story ‘answer’?
  Characters (people)?
  Challenges & actions?
  What to reveal/hide?
MCL
(Glendon Digital Media Lab, 2018b)

## Slide 13
13
3.4. Planning: Research
  General overview: Digital/physical documents
  Interview(s)
      Ethical protocol
      Pre-research
      Focused set of ‘open’ questions ("How" & "why")
      General-specific-general order (warm-up, cool-down)
      Challenges faced & actions done
      Listening, silence, tone
MCL
(Glendon Digital Media Lab, 2018c; York University, 2022)

## Slide 14
14
3.5. Planning: Creating a Script
  Method(s)?
      Interview, recap, report, debate, re-enactment
  Format?
      Level of structure (low, medium, high)
      Exemplars
  External artifacts?
      Music, effects, clips
      Permissions/licenses
MCL
(Glendon Digital Media Lab, 2018d)

## Slide 15
15
3.6. Planning: Pre-Production
  Recording schedule?
      Date, day, time, duration, breaks
      Location, travel
  Locations survey?
      Background noise, disruptions
      Layout (people, power outlets, restrooms)
  Equipment?
      Number of people
MCL
(Glendon Digital Media Lab, 2018f)

## Slide 16
16
3.7. Recording
  Diet
      Avoiding dairy products & carbonated drinks
  Warmup
      Tongue-twisters
  Positioning
      Mic 4-6 inches away mouth
  Method for reading/taking notes
      Electronic device vs printed documents
MCL
(Glendon Digital Media Lab, 2018f)

## Slide 17
17
(continued)
5. Testing recording/mic volume
      Peak volume: -12 dB (up to -6dB)
6. Mitigating distractions
      Smartphones, other talkers
7. Timers
      Audibility/visibility within recording
8. Buffers in recording
      3-5 sec of silence/ambience at beginning & end
MCL
(Glendon Digital Media Lab, 2018f)

## Slide 18
18
3.8. Editing: Asset Management
  File organization?
      Folders (media type, session, person, ...)
      Naming convention
  Music, effects, & clips?
      Copyright-clear vs royalty-free
      Rights owners
      Paid libraries
      Original performances
MCL
(Glendon Digital Media Lab, 2018g)

## Slide 19
19
3.9. Editing: Post-Production
  Audio cleaning?
      Background noise, pops
  Music, effects, & clips?
      Timing
      Mood
  Gain? (Change to recording volume)
      Volume for primary audio (speech): -12 to -6 dB
      Volume for secondary audio (music): -24 to -18 dB
MCL
(Glendon Digital Media Lab, 2018g)

## Slide 20
20
3.10. Publishing
  Channel(s)?
      Coursework: Course-content system
      General: Services with free/paid plans, such as
      Buzzsprout
      Riverside
      Soundcloud
      Spotify
      YouTube
MCL

## Slide 21
21
4. Recording (Zoom H4n)
Best practices apply to all devices
MCL

## Slide 22
22
4.1. Zoom H4n: Features
  Input options: Built-in mics and/or external mics
  Recording-area shapes: 90-degrees or 120-degrees
      Front-facing or front-and-back-facing, respectively
  Modes:
      Stereo: Two channels (input directions)
      4CH: Four channels (input directions)
      MTR: Mixed-track recording (play & record at once)
  Built-in storage: SD card
MCL

## Slide 23
23
4.2. Zoom H4n: Basics
  Locate Hold/power button (left side, bottom)
  Slide button toward I/O icon and hold (2 sec)
  Wait 2-3 min for device to power on
  Locate Menu button & scroll wheel (right side, top)
  Use to Menu & wheel to navigate/select screens
      Wheel turn: Move highlighter
      Wheel press: Select highlighted option
      Menu press: Cancel & return to prior screen
MCL

## Slide 24
24
(continued)
6. Navigate/select “Mode” -> “Stereo”
7. Return to default screen
8. Locate and press Mic button (front side, left edge)
9. Twist ends of built-in mics to 90 or 120 label
MCL

## Slide 25
25
4.3. Zoom H4n: Prep/Monitoring
  Locate & press Rec button (front side)
  Locate Rec Level volume buttons (right side)
  Speak towards mics as intended/expected
  Observe volume-meters on screen
  Note peak values along dB scale
  Adjust Rec Level (“Mic Volume”) so peaks are ~12 dB
  (Optional) Connect headphones (3.5 mm, left side)
  (Optional) Adjust Vol (output) volume buttons (left side)
MCL

## Slide 26
26
4.4. Zoom H4n: Recording
  (From standby) Press Rec (or Play/Pause) button to start
  (Optional) Press Rec while recording to set marks
  (Optional) Press Play/Pause to pause/resume
  Press Stop button to stop recording
MCL

## Slide 27
27
4.5. Zoom H4n: Playback
  Press Play/Pause to play/pause
  (Optional) Press Prev/Next buttons for marks/tracks
  (Optional) Use Menu & wheel to navigate folders
MCL

## Slide 28
28
4.6a. Zoom H4n: File Transfer (Cable)
  Connect USB cable (Micro-USB port, left side)
  Connect cable to computer (USB-A port)
  Navigate/select “USB” -> “Storage”
  (Computer) Open H4N_SD disk drive
  (Computer) Navigate to appropriate folder
  Primary-level folders: 4CH, MTR, Stereo
  Secondary-level folders: Folder01 to Folder10
  (Computer) Copy and paste files (WAV or MP3)
MCL

## Slide 29
29
4.6b. Zoom H4n: File Transfer (Card)
  Slide Hold/Power button to I/O icon & hold (2 sec)
  Remove SD card from slot (right side, bottom)
  Insert card into computer
  (Computer) Open H4N_SD disk drive
  Navigate to appropriate folder
  Primary-level folders: 4CH, MTR, Stereo
  Secondary-level folders: Folder01 to Folder10
  (Computer) Copy and paste files (WAV or MP3)
MCL

## Slide 30
30
4.7. Zoom H4n: Resources
  York University Libraries - Media Creation Lab
      http://bit.ly/mcl-yu
  Zoom
      https://www.zoom.jp/helpcenter/en/products/H4nProBlack/
MCL

## Slide 31
31
5. Recording Practice
Using what you know and have
MCL

## Slide 32
32
5.1. Practice: Story Question
  How did your favourite works of fiction make you feel (the first time you experienced it)?
      Name?
      Context of first experience?
      Conflict(s) in story? (avoid spoilers)
      Emotion(s) experienced?
      Impact?
  (Alternative) Consider another topic
MCL

## Slide 33
33
5.2. Practice: Tips
  Wait 3-5 sec to start talking & stop recording
  Incorporate (repeat) questions being answered
  Include pauses between answers to questions
  Avoid sound-reflecting surfaces
  (If applicable) Cover in blanket to limit echoes
MCL

## Slide 34
34
6. Editing (Audacity)
Power to craft using open-source means
MCL

## Slide 35
35
6.1. Audacity: Overview
  Open-source: Free, established community
  Compatibility: Windows, Mac, Linux
      https://www.audacityteam.org/download/
  Plugins: Support for more audio formats (M4A)
      https://support.audacityteam.org/basics/installing-ffmpeg
  Standard features: Recording, audio effects
MCL

## Slide 36
36
6.2. Audacity: Installation
Windows​
  Open executable-file (*.exe) ​
  Follow prompts of Setup Wizard
macOS
  (If applicable) Open package file (*.pkg)​
  Open disk-image file (*.dmg)​
  (In window) Drag Audacity icon to Applications shortcut
MCL

## Slide 37
37
6.3. Audacity: UI Overview
  Menu bar: File, Effect, View
  Toolbar: Playback, recording, selection, zoom
  Volume meters​: Input levels & output levels
  Timeline​
  Canvas: Tracks/lanes & clips within
  Info panel: Project rate, timestamps, playback speed
MCL

## Slide 38
38
6.4. Audacity: Importing & Lanes
  File -> Import ... -> Audio
      Default: Imported files have separate tracks/lanes
      Lanes have separate control panels
      Solo button: Mutes all other lanes
MCL

## Slide 39
39
6.5. Audacity: Three Lines
  Marker: Black vertical line (at project start by default)
      Click body of track/clip or click Skip To buttons
  Skimmer:​ White vertical line ​
      Appears while project stopped​
      Move cursor along timeline
  Playhead​: Green triangle with black vertical line ​
      Appears while project playing or paused
      Click timeline or click Play button (plays from marker)
MCL

## Slide 40
40
6.6. Audacity: Playback
  Pause [P]​
      Freezes/unfreezes playhead at position in timeline​
  Play [spacebar]​
      Plays from marker position ​
  Stop​
      Clears playhead, enables editing (clip-selection)
MCL

## Slide 41
41
6.7. Audacity: Clip Selection
Select by clip-head (section with title)​
  Single-click head to select clip
Select by clip-body (waveforms)​
  Double-click body to select clip
Select by control-panel (single-clip lane)
  Click Select button to select entire lane
MCL

## Slide 42
42
6.8. Audacity: Clip Arrangment
Click & Drag (need sufficient space)
  Click clip-head & hold
  Drag clip left/right
Cut & Paste (need sufficient space)
  Select clip​
  Right-click​ clip & select Cut [Ctrl/Cmd + X]​
  Click lane (set marker)​
  Right-click lane & select Paste [Ctrl/Cmd + V]
MCL

## Slide 43
43
6.9. Audacity: Clip Trimming
Split & Delete
  Set marker
  Right-click clip & select Split Clip
  Select unwanted clip & press Backspace or Delete key
Drag Edge
  Point to edge (between clip-head & nearest waveform)​
  Look for double-arrow cursor​
  Click & drag edge inward
MCL

## Slide 44
44
6.10. Audacity: Monitoring Volume
  Watching volume meter​ is important
  Blue lines mark (local) peaks
  Ideal volume (peak values):
  Primary audio (speech): -12 dB to -6 dB
  Secondary audio (music): -24 dB to -18 dB
MCL

## Slide 45
45
6.11. Audacity: Editing Volume
Normalize function (set volume to dB value)
  Select clip​
  Open Effect -> Volume & Compression
  Select Normalize … function​
  (Window) Set Normalize peak amplitude to [-12] dB​
Track-wide adjustment (change by dB amount)​
  Click & drag slider in +/- scale of lane control-panel
MCL

## Slide 46
46
6.12. Audacity: Clip Fading
Fading functions
  Select portion of clip​ (click & drag)
  Open Effect menu​
  Select Fading
  Select appropriate function
MCL

## Slide 47
47
6.13. Audacity: Reducing BG Noise
Noise Reduction function
  Select portion of clip​ with background noise (sample)
  Open Effect -> Noise Removal and Repair
  Select Noise Reduction … function​
  (Window) Click Get Noise Profile
  Repeat Steps 2 & 3
  Adjust values (Noise reduction) & click Preview button
  Click OK button
MCL

## Slide 48
48
6.14. Audacity: Recording
  Click Audio Setup button (toolbar)
  Select Recording Device & select device from list
  Click Record Meter (mic icon) button
  Select Start Monitoring & speak as intended/expected
  (Optional) Adjust Recording Level slider (volume meter)
  Click Record button [R or Shift + R for new track/lane)
  (Optional) Click Pause button to pause/resume
  Click Stop button
MCL

## Slide 49
49
6.14a. Audacity: Recording with H4n
  (Recommended) Turn off H4n
  Connect USB cable (Micro-USB port, left side)
  Connect cable to computer (USB-A port)
  Navigate/select “Audio I/F”
  Select “Frequency” -> “48kHz”
  “44.1kHz” is possible with macOS computer
  Select “Connect”
MCL

## Slide 50
50
(continued)
(macOS) Ensure computer has matching frequency:
  Open Applications -> Utilities folder
  Open Audio MIDI Setup app
  Select H4 in sidebar
  Set Format to 48,000 Hz
MCL

## Slide 51
51
(continued)
Set up H4n in Audacity:
  Select Audio Setup -> Recording Device -> Microphone (H4)
  Select Record Meter (icon) -> Start Monitoring
  (Zoom H4n) Adjust Rec Level as needed
  Press Record button start recording
  (Optional) Press Pause button to pause
  Press Stop button to stop recording
MCL

## Slide 52
52
6.15. Audacity: Saving & Exporting
Saving (project file unique to Audacity)
  Open File​ -> Save Project
  Select either Save Project or Save Project As ...
  Set location & name
Exporting (standalone file in standard format)
  Open File -> Export
  Select Export as [format]
  Set location & name
MCL

## Slide 53
53
7. Editing Practice
Experiment
MCL

## Slide 54
54
7.1. Editing Practice
  Consider sharing recordings
  Edit single recording
  Edit entire recordings sequence
  Group quotes/phrases by category (topic, theme)
MCL

## Slide 55
55
References
MCL

## Slide 56
56
Britannica, T. E. of E. (2010). broadcasting summary. In Encyclopedia Britannica. https://www.britannica.com/summary/broadcasting
Britannica, T. E. of E. (2021). podcast. In Encyclopedia Britannica. https://www.britannica.com/art/podcast
Christensen, C. (2019, November 8). Clay Christensen: The Jobs to Be Done theory (Hubspot Marketing, Interviewer) [Video]. https://youtu.be/Stc0beAxavY
DARPA. (n.d.). ARPANET. https://www.darpa.mil/about-us/timeline/arpanet
Glendon Digital Media Lab. (2018a, October 24). Glendon Digital Storytelling Workshop 01: Plan your project with the end-use in mind [Video]. YouTube. https://youtu.be/vG0Lxi58HTE
Glendon Digital Media Lab. (2018b, October 24). Glendon Digital Storytelling Workshop 02: From Topic to Story [Video]. YouTube. https://youtu.be/YqzxXRysAsc
MCL

## Slide 57
57
Glendon Digital Media Lab. (2018c, October 24). Glendon Digital Storytelling Workshop 03: Conducting effective research [Video]. YouTube. https://youtu.be/YHTMnW6Epd4
Glendon Digital Media Lab. (2018d, October 24). Glendon Digital Storytelling Workshop 04: The Shooting Script [Video]. YouTube. https://youtu.be/fsSTDBpTa0E
Glendon Digital Media Lab. (2018e, October 25). Glendon Digital Storytelling Workshop 05: Pre-Production [Video]. YouTube. https://youtu.be/8p95qZWW4DY
Glendon Digital Media Lab. (2018f, October 25). Glendon Digital Storytelling Workshop 08: Writing, recording voice-Over narration [Video]. YouTube. https://youtu.be/_Dlj1eN9-Ps
Glendon Digital Media Lab. (2018g, October 25). Glendon Digital Storytelling Workshop 09: Video editing [Video]. YouTube. https://youtu.be/d0BIelNKRw0
MCL

## Slide 58
58
Wikipedia. (2022a). Podcast. In Wikipedia. https://en.wikipedia.org/w/index.php?title=Podcast&oldid=1110673143
Wikipedia. (2022b). iPod. In Wikipedia. https://en.wikipedia.org/w/index.php?title=IPod&oldid=1113139275
York University. (2022, October 5). Veteran adjunct professor, writer, interviewing trainer publishes new book. YFile. https://yfile.news.yorku.ca/2022/10/05/veteran-adjunct-professor-writer-interviewing-trainer-publishes-new-book/
MCL

## Slide 59
59
Content by Tim Huynh
This work is licensed under a
Creative Commons Attribution-NonCommercial 4.0 International License.
MCL