## Slide 1
1

## Slide 2
2
Contents
1.
Overview & Power
3
2.
Input
10
3.
Output
17
4.
Recording & Playback
25
5.
Usage with Computer
29
References
33
MCL

## Slide 3
3
1. Overview & Power
MCL

## Slide 4
4
1.1. Overview
  Handy/field recorder
  Serious musicians: Live/studio performances
  Interviews, podcasts
  Standalone microphone / audio interface
  Buttons including Menu button & scroll dial
  Press Menu to open main menu, cancel/return
  Scroll dial to highlight, press to select
MCL

## Slide 5
5
1.2. Turning On/Off
  Power button on left side
  Slide to I/O icon & hold for 2 sec
  Startup / shutdown time: ~2 min
  Correlation(?) to storage capacity of SD/SDHC card
  Compatible cards: 512 MB - 32 GB
(Zoom, 2016)
MCL

## Slide 6
6
1.3. Power Options
  AC adapter (bottom): Plug to power socket
  Batteries (back side): Two AA batteries
  Bus power (left side): USB cable to computer
MCL

## Slide 7
7
1.3.a. Power Options: AC adapter
  Port on bottom
  5 volts, 1 amps
MCL

## Slide 8
8
1.3.b. Power Options: AA Batteries
  Housing component on back
  Alkaline or nickel-metal hydride (Ni-MH, 2500 mAh)
  Menu -> System -> Battery -> [Alkaline/Ni-MH]
  Stamina mode: Longer battery life vs limited functions
  Open cover & slide Stamina button to On
  Battery life: Recommend duration is ~3-4 hrs
  Alkaline: ~5.5 hrs (~8 hrs in Stamina mode)
  Ni-MH: ~7.5 hrs (~10 hrs in Stamina mode)
(Zoom, n.d.)
MCL

## Slide 9
9
1.3.c. Power Options: Bus Power
  Mini-USB port on left side
  Connect cable to computer with USB-A port/adapter
  H4n can be turned off
  While turned on, select Menu -> USB -> [mode]
  Storage: Transfer files to computer
  Audio I/F (interface): Use device only as mic
MCL

## Slide 10
10
2. Input
MCL

## Slide 11
11
2.1. Core Concepts
  Channel: Representation of sound to/from any point
  Mono: One channel, file has combined L/R section
  Stereo: Two channels, file has separate L/R sections
  H4n Pro mode selection: Menu -> Mode -> [mode]
  Stereo: Record two channels
  4CH: Record four channels
  MTR: Play/record multiple tracks at same time
MCL

## Slide 12
12
2.2. Input Options
  Built-in mics (top)
  External 3.5 mm mic (back side)
  External 1/4 in and/or XLR mics (bottom)
  In Input section of front, press Mic, 1, or 2 button
  4CH mode automatically selects Mic, 1, & 2
MCL

## Slide 13
13
2.2.a. Input Options: Built-in Mics
  Twin mics on top in X/Y configuration
  90- or 120-degree pickup pattern (recording area)
  Twist both mic knobs to 90 or 120 label
  90: One audio source (e.g. person)
  Place parallel to floor & point to source
  120: Two+ audio sources (e.g. two persons)
  Place perpendicular to floor & between sources
MCL

## Slide 14
14
2.2.b. Input Options: 3.5 mm Mic
  3.5 mm port on back
  Uses cases:
  Condenser/desktop mics
  Lapel/lavalier mics
  Receiver of wireless mic system
  Automatic override of built-in mics
MCL

## Slide 15
15
2.2.c. Input Options: 1/4-in, XLR mics
  Two combo ports (1/4 in or XLR) on bottom
  Press Push lever to release
  Use cases:
  Mics, instruments (guitars, keyboards)
  Receiver of wireless mic system
  Inputs 1 & 2 share volume by default
  Menu -> Input -> 1/2 Link -> [On/Off]
  Inputs 1 & 2 each record one channel
  One-sided stereo recording
MCL

## Slide 16
16
2.3. Recording Level (Volume)
  Rec Level buttons (right side): Change [Input] Level
  Press Input button on front to match input
  Resting, standby (ideal), or recording state
Preview mic level before recording:
  Press Rec button to enter standby
  Position device/mic as intended
  Produce sound as intended & observe on-screen meters
  Adjust [Input] Level so peaks are at -12 dB mark (+/- 3)
MCL

## Slide 17
17
3. Output
MCL

## Slide 18
18
3.1. Output Options
  Built-in speaker (back side)
  Headphone/line-out (left side)
MCL

## Slide 19
19
3.1.a. Output Options: Built-in Speaker
  Built-in speaker on back side
  Standalone or audio-interface mode
MCL

## Slide 20
20
3.1.b. Output Options: Headphone/Line
  3.5 mm port on left side
  Use cases:
  Headphones
  External speakers (amplification)
  Sound board/mixer
MCL

## Slide 21
21
3.2. Output Volume
  Vol buttons on left side: Change (output) Volume
  Resting, standby, recording, or playback states
  Independent of Rec Level
MCL

## Slide 22
22
3.3. File Formats
  WAV or MP3
  WAV: Higher quality
  Create recording marks (bookmarks for playback)
  MP3: Smaller file-size
Format selection
  Menu - > Rec -> Rec Format -> [format]
  (Main screen) Press WAV/MP3 button -> [format]
MCL

## Slide 23
23
3.4. File Organization
  Recording modes have separate folders & sub-folders
  Stereo -> [Folder01 ... Folder10] -> [file]
  4CH -> [Folder01 ... Folder10] -> [files]
  4CH recordings: Twin files appended with I or M
  MTR -> ProjXYZ -> [file]
MCL

## Slide 24
24
3.5. Folder/File Selection
Select sub-folder (within current mode folder)
  Menu -> Folder
  (Main screen) Press Folder button
Select file in current sub-folder
  Menu -> File
  (Main screen) Press File button
MCL

## Slide 25
25
4. Recording & Playback
MCL

## Slide 26
26
4.1. Accessories
  Tripod with 1/4 in screw
  Fur windshield
MCL

## Slide 27
27
4.2. Rec Button
  Enter standby state
  Preview recording level
  Start recording from standby state
  (Alternative) Press Play button
  (Optional) Set marks while recording (WAV only)
  Press before relevant points
  Can have 99 marks
  Note button doesn’t function as pause button
MCL

## Slide 28
28
4.3. Other Buttons
  Stop button: Stop recording; stop playback
  Play/Pause button:
  Recording: Start (from standby), pause/resume
  Playback: Play/pause/resume playback
  Skip buttons: Skip to next/previous file
  (If applicable) Skip to next/previous mark within file
  Key Hold (left side): Disables button input
  Slide power switch to Hold
MCL

## Slide 29
29
5. Usage with Computer
MCL

## Slide 30
30
5.1. File Transfer
Transfer by USB cable
  Insert USB cable into mini-USB port on left side
  Connect cable to computer & turn off H4n
  (H4n) Select Storage & (computer) locate H4N_SD drive
Transfer by SD card
  Remove SD card from covered slot on right side
  Insert into computer with slot/adapter
  (Computer) Locate H4N_SD drive
MCL

## Slide 31
31
5.2. USB Mic
Setup on H4n
  (Recommended) Turn off H4n
  Connect USB cable (Micro-USB port, left side)
  Connect cable to computer
  Select Audio I/F
  Select Frequency -> 48kHz (44.1kHz possible on Mac)
  Select Connect
  H4n appears on computer as H4
MCL

## Slide 32
32
(continued)
Setup on Mac (macOS)
  Open Applications -> Utilities -> Audio MIDI Setup
  Or use Spotlight Search to find Audio MIDI Setup
  Select H4 (2 ins / 0 outs) in sidebar
  Set Format drop-down to equivalent frequency on H4n
  (H4n) 44.1kHZ = (Mac) 44,100 Hz
  (H4n) 48kHZ = (Mac) 48,000 Hz
  Discrepancies: higher/lower pitch of recordings
MCL

## Slide 33
33
References
MCL

## Slide 34
34
Zoom. (n.d.). Zoom H4n Pro Black. https://zoomcorp.com/en/ca/handheld-recorders/handheld-recorders/h4n-pro/
Zoom. (2016). H4n/H4nPro operation confirmed SD/SDHC cards. https://zoomcorp.com/media/documents/H4n_H4nPro_compatible_cards_en_2.pdf
MCL

## Slide 35
35
Content by Tim Huynh
This work is licensed under a
Creative Commons Attribution-NonCommercial 4.0 International License.
MCL